## Slide 1: Preparations for the Testing of ITk Silicon Strip Sensors
Andrew Musgrave

## Slide 2: Inner Tracking Detector
The inner tracking detector is a large area silicon sensor
It must have full coverage (hermeticity)
It consists of pixel detectors on the inner layers and strip detectors on the outer layers

## Slide 3: The High Luminosity LHC
  The HL-LHC will increase luminosity from 1x 1034 cm-2s-1 to 7.5 x 1034 cm-2s-1
  The total dataset will be increased by an order of magnitude
  Installation will take place in 2024-2026

## Slide 4: Track Reconstruction
Each time an ionizing particle passes through a detector layer a vertex is recorded
The sensors on each side of a layer are angled relative to each other
A sophisticated algorithm is used to reconstruct the particle tracks from these vertices

## Slide 5: Silicon Strip Detector
Consists of n+ implants in a p substrate
The implants are AC coupled to aluminum strips
Held in reverse bias of up to 700V
An ionizing particle passing through the detector frees charge carriers and induces a voltage spike in the sensor strip

## Slide 6: Readout Chips
ABC130 or ABC* chips are used to gather data from the strip sensors
Each ABC receives input from 256 strips
The ABC is responsible for digitizing data and managing readout

## Slide 7: Sensor Testing at Carleton
5000 sensors will pass through Carleton by the end of 2023
Visual inspection
Basic metrology: sensor flatness
Leakage Current: IV curve
Full depletion voltage: CV curve

## Slide 8: Environmental Monitoring
A Raspberry Pi is used to monitor the conditions in the Clean Room
I maintained this system and implemented a database to record and manage environmental data

## Slide 9: Sensor Measurements
I assisted in measuring the IV and CV curves for a pair of sensors
Breakdown voltage and full depletion voltage were observed

## Slide 10: Analog Test Code
Analog tests of the ABC130 produce long and unreadable output files
Root scripts are used to parse this output and produce plots

## Slide 11: ITSDAQ Installation
ITSDAQ is the data acquisition software for the ABC130 and ABC*
It was installed on the clean room computer for use with the single chip tester

## Slide 12: A Learning Experience
Through this opportunity I have learned many things, including:
How to use the ROOT data analysis framework
How to work in a clean room environment
A great deal about silicon tracking detectors!