## Slide 1: Development of a Guided User Interface; egs_bachy GUI
Shannon Jarvis
Supervisor: Rowan Thomson
August 27, 2019
Summer Student Presentations

## Slide 2: Outline
Background information on brachytherapy
Description of egs_brachy code
Purpose and process of egs_brachy GUI (Guided User Interface)

## Slide 3: Brachytherapy
A type of radiation therapy where radioactive sources are placed near or within a tumor
  Used to treat cancer
A treatment plan is created by assessing the dose
  Dose: energy deposited per unit mass in tissue
  due to radiation
Patient CT Image of chest with location of brachytherapy sources circled

## Slide 4: Clinical Brachytherapy
Approximations are used to calculate the dose;
  Patient is an infinite volume of water
  Effect of each brachytherapy source considered individually
Doesn’t accurately represent the patient

## Slide 5: egs_brachy
Developed by the Carleton Laboratory for Radiotherapy Physics
Model-Based Dose Calculation Algorithm
  Uses a patient specific model to calculate dose
Patient is represented by a voxelized virtual model
  3-D grid of voxels
Requires a specific format of input files

## Slide 6: Purpose of egs_brachy GUI
Guided User Interface (GUI) to integrate egs_brachy with clinical data
  Clinical CT Data
    Series of cross-sectional images (slices)
    Organ contours
    Brachytherapy source
CT Image of a Test Case

## Slide 7: Process of egs_brachy GUI
1) Read in clinical data
2) Create a patient model
4) Launch egs_brachy
5) Convert egs_brachy output to clinical format
3) Generate egs_brachy input files

## Slide 8: 1) Read in Clinical Data
Standard format
  DICOM = Digital Imaging and Communications in Medicine
  Hexadecimal file
An 8 character sequence, called a tag, is used to identify all data in the file
Information is extracted from all relevant tags

## Slide 9: CT Image Data
Each CT image consists of a matrix of pixels that represents each volume element (voxel)
Pixels are measured in Hounsfield Units (HU)
  Units of radiodensity
  Related to the attenuation coefficient
Each CT machine has a calibration to convert HU to density

## Slide 10: 2) Create a patient model
Process begins with an empty patient model
Number of voxels is based on the number and size of CT images

## Slide 11: 2) Create a patient model
Process begins with an empty patient model
Each voxel has a corresponding pixel value
Number of voxels is based on the number and size of CT images

## Slide 12: 2) Create a patient model
Process begins with an empty patient model
Each voxel has a corresponding pixel value
Pixel value (HU) is converted to density
Number of voxels is based on the number and size of CT images
Using the CT machine specific conversion

## Slide 13: 2) Create a patient model
Process begins with an empty patient model
Each voxel has a corresponding pixel value
Pixel value (HU) is converted to density
Number of voxels is based on the number and size of CT images
Using the CT machine specific conversion
Each voxel is mapped to an organ using the physician drawn contours

## Slide 14: Physician Drawn Organ Contours

## Slide 15: 2) Create a patient model
Process begins with an empty patient model
Each voxel has a corresponding pixel value
Pixel value (HU) is converted to density
Number of voxels is based on the number and size of CT images
Using the CT machine specific conversion
Each voxel is mapped to an organ using the physician drawn contours
A tissue assignment scheme determines the tissue of each voxel

## Slide 16: Breast Tissue Assignment Scheme
0.947
Organs in the patient
Tissues
Deering, S. (2017). Monte Carlo Dose Calculations for Permanent Breast Seed Implant Brachytherapy (Master's thesis).
Retrieved from https://curve.carleton.ca/450b147b-d385-47a3-8f12-c0a479f2ece7 (p 21) [Modified]
Notes: Top identifies the contours in the patient

## Slide 17: 3) Create egs_brachy input files
The input files contain:
  Patient model
  Parameters to run the simulation
  Location and type of brachytherapy source

## Slide 18: 4) Launch egs_brachy
Monte Carlo code
Models radiation transport and energy deposition
Calculates the dose and error delivered to each voxel

## Slide 19: 5) Convert egs_brachy output to clinical format
Data converted to the DICOM format
  Can be read by clinicians
Dose metrics are calculated
  Helps to evaluate the treatment plan

## Slide 20: Screenshot of egs_brachy GUI
1

## Slide 21: Screenshot of egs_brachy GUI
2

## Slide 22: Screenshot of egs_brachy GUI
3

## Slide 23: Screenshot of egs_brachy GUI
4

## Slide 24: Screenshot of egs_brachy GUI
5
After egs_brachy has finished running

## Slide 25: Thank you

## Slide 27: What I Learned
C++ and Qt
Using linux
Introduction to medical physics
And much more!